## Slide 1: Chapter 6: Medium Access Control Layer
Notes: <number>

## Slide 2: Chapter 6: Roadmap
Overview
Wireless MAC protocols
  Carrier Sense Multiple Access
  Multiple Access with Collision Avoidance (MACA) and MACAW
  MACA By Invitation
  IEEE 802.11
  IEEE 802.15.4 and ZigBee
Characteristics of MAC Protocols in Sensor Networks
  Energy Efficiency
  Scalability
  Adaptability
  Low Latency and Predictability
  Reliability
Contention-Free MAC Protocols
Contention-Based MAC Protocols
Hybrid MAC Protocols
Notes: <number>

## Slide 3: Medium Access Control
In most networks, multiple nodes share a communication medium for transmitting their data packets
The medium access control (MAC) protocol is primarily responsible for regulating access to the shared medium
The choice of MAC protocol has a direct bearing on the reliability and efficiency of network transmissions
  due to errors and interferences in wireless communications and to other challenges
Energy efficiency also affects the design of the MAC protocol
  trade energy efficiency for increased latency or a reduction in throughput or fairness
Notes: <number>

## Slide 4: Overview
Responsibilities of MAC layer include:
  decide when a node accesses a shared medium
  resolve any potential conflicts between competing nodes
  correct communication errors occurring at the physical layer
  perform other activities such as framing, addressing, and flow control
Second layer of the OSI reference model (data link layer) or the IEEE 802 reference model (which divides data link layer into logical link control and medium access control layer)

## Slide 5: MAC Protocol Categorization

## Slide 6: Contention-Free Medium Access
Collisions can be avoided by ensuring that each node can use its allocated resources exclusively
Examples of fixed assignment strategies:
  FDMA: Frequency Division Multiple Access
    the frequency band is divided into several smaller frequency bands
    the data transfer between a pair of nodes uses one frequency band
    all other nodes use a different frequency band
  TDMA: Time Division Multiple Access
    multiple devices to use the same frequency band
    relies on periodic time windows (frames)
      frames consist of a fixed number of transmission slots to separate the medium accesses of different devices
      a time schedule indicates which node may transmit data during a certain slot

## Slide 7: Contention-Free Medium Access
Examples of fixed assignment strategies (contd.):
  CDMA: Code Division Multiple Access
    simultaneous accesses of the wireless medium are supported using different codes
    if these codes are orthogonal, it is possible for multiple communications to share the same frequency band
    forward error correction (FEC) at the receiver is used to recover from interferences among these simultaneous communications
Fixed assignment strategies are inefficient
  it is impossible to reallocate slots belonging to one device to other devices if not needed in every frame
    generating schedules for an entire network can be a taunting task
    these schedules may require modifications every time the network topology or traffic characteristics in the network change

## Slide 8: Contention-Free Medium Access
Dynamic assignment strategies: allow nodes to access the medium on demand
  polling-based protocols
    a controller device issues small polling frames in a round-robin fashion, asking each station if it has data to send
    if no data to be sent, the controller polls the next station
  token passing
    stations pass a polling request to each other (round-robin fashion) using a special frame called a token
    a station is allowed to transmit data only when it holds the token
  reservation-based protocols
    static time slots used to reserve future access to the medium
    e.g., a node can indicate its desire to transmit data by toggling a reservation bit in a fixed location
    these often very complex protocols then ensure that other potentially conflicting nodes take note of such a reservation to avoid collisions

## Slide 9: Contention-Based Medium Access
Nodes may initiate transmissions at the same time
  requires mechanisms to reduce the number of collisions and to recover from collisions
Example 1: ALOHA protocol
  uses acknowledgments to confirm the success of a broadcast data transmission
    allows nodes to access the medium immediately
    addresses collisions with approaches such as exponential back-off to increase the likelihood of successful transmissions
Example 2: slotted-ALOHA protocol
  requires that a station may commence transmission only at predefined points in time (the beginning of a time slot)
  increases the efficiency of ALOHA
  introduces the need for synchronization among nodes

## Slide 10: Contention-Based Medium Access
Carrier Sense Multiple Access (CSMA)
  CSMA with Collision Detection (CSMA/CD)
    sender first senses the medium to determine whether it is idle or busy
      if it is found busy, the sender refrains from transmitting packets
      if the medium is idle, the sender can initiate data transmission
  CSMA with Collision Avoidance (CSMA/CA)
    CSMA/CD requires that sender aware of collisions
    instead, CSMA/CA attempts to avoid collisions in the first place

## Slide 11: Hidden and Exposed Terminal Problems
Hidden-terminal problem
  senders A and C are able to reach B, but cannot overhear each other’s signals
  it is possible for A and C to transmit data to B at the same time, causing a collision at B, without being able to directly detect this collision
Exposed-terminal problem
  C wants to transmit data D, but decides to wait because it overhears an ongoing transmission from B to A
  B’s transmission could not interfere with data reception at C

## Slide 12: Carrier Sense Multiple Access
Nodes first sense the medium before they begin a transmission (reduces number of collisions)
Non-persistent CSMA
  node is allowed to immediately transmit data once medium is idle
  if the medium is busy, the node performs a back-off operation
    wait for a certain amount of time before attempting to transmit again
1-persistent CSMA
  node wishing to transmit data continuously senses the medium for activity
  once the medium is found idle, the node transmits data immediately
  if a collision occurs, the node waits for a random period of time before attempting to transmit again

## Slide 13: Carrier Sense Multiple Access
p-persistent CSMA
  node continuously senses the medium
  node transmits data with a probability p once the medium becomes idle
  delays transmission with a probability 1 − p
  random back-off values are either continuous values in the case of un-slotted CSMA or multiples of a fixed slot size in slotted CSMA
CSMA/CA (CSMA with Collision Avoidance)
  nodes sense the medium, but do not immediately access the channel when it is found idle
  instead, a node waits for a time period called DCF interframe space (DIFS) plus a multiple of a slot size
  in case there are multiple nodes attempting to access the medium, the one with the shorter back-off period will win

## Slide 14: Carrier Sense Multiple Access
Example:
  node A waits for DIFS + 4 ∗ s (where s represents the slot size), while node B’s back-off is DIFS + 7 ∗ s
  once node A begins with its transmission, node B freezes its own back-off timer and resumes the timer after node A completes its transmission plus another period of DIFS
  once node B’s back-off timer expires, it can also begin its transmission

## Slide 15: MACA and MACAW
Multiple Access with Collision Avoidance (MACA)
  dynamic reservation mechanism
  sender indicates desire to send with ready-to-send (RTS) packet
  intended receiver responds with clear-to-send (CTS) packet
  if sender does not receive CTS, it will retry at later point in time
  nodes overhearing RTS or CTS know that reservation has taken place and must wait (e.g., based on the size of data transmission)
  address hidden terminal problem and reduces number of collisions
MACA for Wireless LANs (MACAW)
  receiver responds with acknowledgment (ACK) after data reception
    other nodes in receiver’s range learn that channel is available
  nodes hearing RTS, but not CTS do not know if transmission will occur
    MACAW uses data sending (DS) packet, sent by sender after receiving CTS to inform such nodes of successful handshake

## Slide 16: MACA By Invitation
In MACA-BI, destination device initiates data transfers by sending a Ready To Receive (RTR) packet to the source
  source then responds with the data message
Compared to MACA, MACA-BI reduces overhead
  increases the theoretical maximum throughput
  depends on the destination knowing when to receive data
Source nodes can use an optional field within the data message to indicate the number of queued messages
  providing the destination with an indication that more RTS packets will be required

## Slide 17: IEEE 802.11
Published in 1999 by the Institute of Electrical and Electronics Engineers (IEEE)
  specifies the physical and data link layers of the OSI model for wireless connections
Often referred to as Wireless Fidelity (Wi-Fi)
  certification given by Wi-Fi Alliance, a group that ensures compatibility between hardware devices that use the 802.11 standard
Wi-Fi combines concepts found in CSMA/CA and MACAW, but also offers features to preserve energy
Two modes of operation
  Point Coordination Function (PCF) mode
    communication among devices goes through a central entity called an access point (AP) or base station (BS): managed mode
  Distributed Coordination Function (DCF) mode
    devices communicate directly with each other: ad-hoc mode

## Slide 18: IEEE 802.11
IEEE 802.11 is based on CSMA/CA
  before a node transmits, it first senses the medium for activity
  the node is allowed to transmit, if the medium is idle for at least a time period called the DCF interframe space (DIFS)
  otherwise the device executes a back-off algorithm to defer transmission to a later time
  this algorithm randomly selects a number of time slots to wait and stores this value in a back-off counter
  for every time slot that passes without activity on the network, the counter is decremented and the device can attempt transmission when this counter reaches zero
  if activity is detected before the counter reaches zero, the device waits until the channel has been idle for a period of DIFS before it continues to decrement the counter value

## Slide 19: IEEE 802.11
After a successful transmission
  receiver device responds with an acknowledgment after waiting for a time period called the short interframe space (SIFS)
  the value of SIFS is smaller than the value of DIFS to ensure that no other device accesses the channel before the receiver can transmit its acknowledgment
Once a node A makes a reservation using RTS and CTS control messages
  another neighboring node B, overhearing the RTS message, must refrain from accessing the medium until node A’s transmission has been completed and acknowledged
  however, this would mean that node B has to continuously sense the medium to detect when it becomes idle again

## Slide 20: IEEE 802.11
Instead, A’s RTS message carries the size of the data it will transmit
  allowing node B to estimate how long the transmission will take and to decide whether to enter a low-power sleep mode
  some neighboring nodes may only overhear CTS (but not RTS), therefore, the data size is also carried in the CTS message
  using the data size information, neighboring nodes set a network allocation vector (NAV) that indicates how long the medium will be unavailable
    reduces the need for continuously sensing the medium, allowing a node to save power

## Slide 21: IEEE 802.11

## Slide 22: IEEE 802.11
PCF mode
  access point (AP) coordinates channel access to ensure collision-free communication
    periodically broadcasts a beacon to its client devices (includes list of devices with data pending at AP)
  during contention-free period, AP transmits these packets to its client devices
  AP can also poll client devices to allow them to initiate data transfers
  AP uses a wait period called the PCF interframe space (PIFS)
    PIFS is shorter than DIFS, but longer than SIFS
    ensures that PCF traffic has priority over traffic generated by devices operating in the DCF mode, without interfering with control messages in the DCF mode such as CTS and ACK

## Slide 23: IEEE 802.11
Focus of IEEE 802.11 is on providing fair access to the medium with support for high throughput and mobility
  since devices spend a large amount of time listening to the medium and collisions occur frequently, this standard incurs large overheads, including significant energy costs
Energy consumption problem
  IEEE 802.11 offers a power saving mode (PSM) for devices operating in the PCF mode
  devices can inform the AP that they wish to enter a low-power sleep mode using special control messages
  these devices wake up periodically to receive beacon messages from the AP to determine if they should stay awake to receive incoming messages
  saves energy, but only works in the infrastructure mode and it is not specified when or how long devices should sleep

## Slide 24: IEEE 802.15.4
IEEE 802.15.4
  created for low-power devices in the 868 MHz, 915 MHz, and 2.45 GHz frequency bands
  supports two transmission modes:
    UWB PHY
      bit rates: 110 kbps, 851 kbps (nominal), 6.81 kbps, and 27.24 Mbps
    CSS PHY
      bit rates: 1 Mbps (nominal) and 250 kbps

## Slide 25: ZigBee
Before 802.15.4, ZigBee Alliance worked on low-cost communication technology for low data rates and low power consumption
IEEE and ZigBee Alliance joined forces and ZigBee has become the commercial name for the IEEE 802.15.4 technology
Star mode:
  communication via the Personal Area Network (PAN) coordinator
  synchronized mode (beacon-enabled)
    PAN coordinator periodically broadcasts beacons for synchronization and management
    slotted channel access: device performs random backoff before channel is sensed
      if no activity, node waits until next slot and senses channel again until no activity has been detected for two consecutive slots
      if activity, backoff procedure is repeated
  unsynchronized mode: device access channel immediately when no activity is detected during the first initial backoff time

## Slide 26: ZigBee
Peer-to-peer mode:
  devices are free to communicate directly with each other
  but they still must associate with the PAN coordinator before they can participate in peer-to-peer communication
Data transfer between the device and its PAN coordinator is always initiated by the device
  allows a device to determine when data is transferred and to maximize its energy savings
    when a device wants to send data to the PAN coordinator, it can use the previously described channel access method
    the PAN coordinator transmits data intended for a device only after the device explicitly requested such a transmission
  in both cases, optional acknowledgments can be used to let the PAN coordinator or device know that the transmission was successful

## Slide 27: IEEE 802.15.4 and ZigBee
Challenges:
  standard does not clearly define the operation of the peer-to-peer approach
  in large WSNs, it is unlikely that all devices will be able to use the same PAN coordinator
  standard does allow communication among PAN coordinators, but this again is not well defined

## Slide 28: Characteristics of MAC Protocols in WSNs
Most MAC protocols are built for fairness
  everybody should get an equal amount of resources
  no one should receive special treatment
In a WSN, all nodes cooperate to achieve a common purpose, therefore fairness is less of a concern
Instead, wireless nodes are mostly concerned with energy consumption
Sensing applications may value low latency or high reliability over fairness

## Slide 29: Energy Efficiency
Sensor nodes must operate using finite energy sources, therefore MAC protocols must consider energy efficiency
Common technique: dynamic power management (DPM)
  a resource can be moved between different operational modes such as active, idle, and asleep
  for resources such as the network, the active mode can group together multiple different modes of activity, e.g., transmitting and receiving
Periodic traffic models are very common in WSNs
  significant energy savings can be obtained by putting a device into a low-power sleep mode
  fraction of time a sensor nodes spends in active mode is called the duty cycle
    often very small due to the infrequent and brief data transmissions occurring in most sensor networks

## Slide 30: Energy Efficiency
 | RFM TR1000 | RFM TR3000 | MC13202 | CC1000 | CC2420
Data rate (kbps) | 115.2 | 115.2 | 250 | 76.8 | 250
Transmit current | 12mA | 7.5mA | 35mA | 16.5mA | 17.4mA
Receive current | 3.8mA | 3.8mA | 42mA | 9.6mA | 18.8mA
Idle current | 3.8mA | 3.8mA | 800μA | 9.6mA | 18.8mA
Standby current | 0.7μA | 0.7μA | 102μA | 96μA | 426μA
Characteristics of typical radios used by state-of-the-art sensor nodes

## Slide 31: Energy Efficiency
Reasons for energy inefficiency
  idle listening
  inefficient protocol designs (e.g., large packet headers)
  reliability features (collisions requiring retransmissions or other error control mechanisms)
  control messages to address the hidden-terminal problem
  choice of modulation scheme
  choice of transmission rate
  overemitting

## Slide 32: Scalability
Many wireless MAC protocols have been designed for use in infrastructure-based networks
  access points or controller nodes arbitrate access to the channel and perform some centralized coordination and management functions
Most wireless sensor networks rely on multi-hop and peer-to-peer communications without centralized coordinators
MAC protocols must be able to allow for efficient use of resources without incurring unacceptable overheads, particularly in very large networks
MAC protocols based on CDMA have to cache a large number of code (may be impractical for resource-constrained sensor devices)
WSNs are not only constrained in their energy resources, but also in their processing and memory capacities
Therefore, MAC protocols should not impose excessive computational burden should not require too much memory to save state information

## Slide 33: Adaptability
A key characteristic of a WSN is its ability to self-manage
  adapt to changes in the network
  including changes in topology, network size, density, and traffic characteristics
A MAC protocol for a WSN should be able to gracefully adapt to such changes without significant overheads
This requirement generally favors protocols that are dynamic in nature
  protocols that make medium access decisions based on current demand and network state
Protocols with fixed assignments (e.g., TDMA with fixed-size frames and slots) may incur large overheads due to adaptations of such assignments that may affect many or all nodes in the network

## Slide 34: Low Latency and Predictability
Many WSN applications have timeliness requirements
  sensor data must be collected, aggregated, and delivered within certain latency constraints or deadlines
  example: wildfire detection (sensor data must be delivered to monitoring stations in a timely fashion to ensure timely responses)
MAC protocol design
  choice of frame size and slot allocations in TDMA-based protocols may lead to large delays
  in contention-based protocols, nodes may be able to access the wireless medium sooner (than TDMA), but collisions and the resulting retransmissions incur delays
  choice of MAC protocol can affect how predictable the experienced delay is (expressed as upper latency bounds)
  some contention-based MAC protocols allow the theoretical possibility of starvation

## Slide 35: Reliability
Common requirement for WSNs
MAC protocol design affects reliability
  responsible for detecting and recovering from transmission errors and collisions

## Slide 36: Contention-Free MAC Protocols
Concept:
  allow only one sensor node to access the channel at any given time
  thereby avoiding collisions and message retransmissions
  assuming a perfect medium and environment
    i.e., no other competing networks or misbehaving devices exist that could otherwise cause collisions or even jam a channel
Contention-free protocols allocate resources to individual nodes to ensure exclusive resource access by only one node at any given time
Exposes a number of desirable characteristics
  node knows exactly when it has to turn on its radio
  during all other times, radio can be turned off to preserve energy
  fixed slot allocations impose upper bounds on delay
  difficult to design schedules for large networks
  difficult to handle changes in topology, density, traffic load

## Slide 37: Traffic-Adaptive Medium Access
TRAMA is an example of a contention-free MAC protocol with the goal to increase network throughput and energy efficiency (compared to TDMA)
It uses a distributed election scheme to determine when nodes are allowed to transmit
  based on information about the traffic at each node
  avoids assigning slots to nodes with no traffic to send (increased throughput)
  allows nodes to determine when they can become idle and do not have to listen to the channel (increased energy efficiency)

## Slide 38: Traffic-Adaptive Medium Access
TRAMA assumes a time-slotted channel, where time is dived into:
  periodic random-access intervals (signaling slots)
  scheduled-access intervals (transmission slots)
Random-access intervals
  Neighbor Protocol (NP) is used to propagate one-hop neighbor information among neighboring nodes
    nodes join a network by transmitting during a randomly selected slot
    packets transmitted during these slots are used to gather neighborhood information by carrying a set of added and deleted neighbors
    in case no changes have occurred, these packets serve as “keep-alive” beacons
  NP allows nodes to obtain consistent two-hop topology information

## Slide 39: Traffic-Adaptive Medium Access
Random-access intervals (contd.)
  Schedule Exchange Protocol (SEP) establishes and broadcasts actual schedules (i.e., allocations of slots to a node)
    each node computes a duration SCHEDULE_INTERVAL
      represents the number of slots for which the node can announce its schedule to its neighbors
      this duration depends on the rate at which the node’s applications can produce packets
    at time t, the node then computes the number of slots within [t, t+ SCHEDULE_INTERVAL] for which it has the highest priority among its two-hop neighbors
    the node announces the selected slots and the intended receivers using a schedule packet
    the last slot in this schedule is used to announce the next schedule for the next interval

## Slide 40: Traffic-Adaptive Medium Access
Random-access intervals (contd.)
  Schedule Exchange Protocol (SEP) (contd.)
    example:
      a node’s SCHEDULE_INTERVAL is 100 slots
      the current time (slot number) is 1000
      a possible slot selection for interval [1000, 1100] for this node could be 1011, 1021, 1049, 1050, and 1093
      during slot 1093, the node broadcasts its new schedule for interval [1093, 1193]
    list of intended receivers in the schedule packet is implemented as a bitmap
      length of a bitmap is equal to the number of one-hop neighbors
        each bit in the bitmap corresponds to one particular receiver ordered by its identities
        every node can determine the receiver address based on the bitmap and its list of neighbors

## Slide 41: Traffic-Adaptive Medium Access

## Slide 42: Traffic-Adaptive Medium Access
Summary
  compared to CSMA-based protocols
    reduces the probability of collisions
    increases the sleep time and energy savings
  unlike standard TDMA approaches
    TRAMA divides time into random-access and scheduled-access intervals
    during the random-access intervals
      nodes are awake to either transmit or receive topology information
      the length of the random-access interval affects the overall duty cycle and achievable energy savings of a node

## Slide 43: Y-MAC
Y-MAC uses TDMA-based medium access but for multiple channels
Divides time into frames and slots
  each frame contains a broadcast period and a unicast period
  every node must wake up at the beginning of a broadcast period
  nodes contend for access to the medium during this period
    if there are no incoming broadcast messages, each node turns off its radio awaiting its first assigned slot in the unicast period
    each slot in the unicast period is assigned to only one node for receiving data
Y-MAC uses a receiver-driven model
  can be more energy-efficient under light traffic conditions, because each node samples the medium only in its own receive time slots
  particularly important for radio transceivers, where the energy costs for receiving are greater than for transmitting (e.g., due to sophisticated despreading and error correction techniques)

## Slide 44: Y-MAC
Medium access in Y-MAC is based on synchronous low power listening
The contention window (at beginning of each slot) resolves contention between multiple senders
  a node wishing to send data sets a random wait time (back-off value) within the contention window
  after this wait time, the node wakes up and senses the medium for activity for a certain amount of time
    if the medium is free, the node sends a preamble until the end of the contention window to suppress competing transmissions and the receiver wakes up at the end of the contention window to wait for packets in its assigned slot
    if the medium receives no signal from any of its neighboring nodes, it turns off the radio and returns to the sleep mode

## Slide 45: Y-MAC
Unicast period
  messages are initially exchanged on the base channel
  at the beginning of its receive slot
    a receiver switches its frequency to the base channel
    the node that won the medium in the contention window also uses the base channel to transmit its packet
    the receiver acknowledges this packet (if the acknowledgment request flag was set in the packet)
Broadcast period
  every node tunes to the base channel
  the potential senders take part in the contention process described above

## Slide 46: Y-MAC
Every node polls the medium only during broadcast time slots and its own unicast receive time slots
  makes this approach energy-efficient
  however, under heavy traffic conditions, many unicast messages may have to wait in the message queue or are dropped due to the limited bandwidth reserved for the receiving node
  as a consequence, Y-MAC uses a channel hopping mechanism to reduce packet delivery latency

## Slide 47: Y-MAC
After receiving a packet during its time slot on the base channel, the receiving node hops to the next channel and sends a notification
  it can continue to receive packets on the second channel
  contention for the medium in the second channel is resolved as before
At the end of this slot, the receiving node can decide to hop again to another channel
  until reaching the last channel or
  until no more data is being received
The hopping sequence generation algorithm
  determines the actual hopping sequence among the available channels
  should guarantee that there is only one receiver among one-hop neighbors on any particular channel

## Slide 48: Y-MAC
Summary
  Y-MAC uses slot assignments (such as TDMA)
  communication is receiver-driven to ensure low-energy consumption
    i.e., a receiver briefly samples the medium during its slot and returns to the sleep mode if no packets arrive
  uses multiple channels
    to increase the achievable throughput
    to reduce delivery latency
  main drawbacks of the Y-MAC approach:
    has the same flexibility and scalability issues as TDMA (i.e., fixed slot allocations)
    requires sensor nodes with multiple radio channels

## Slide 49: DESYNC-TDMA
DESYNC is a self-organizing desynchronization algorithm
DESYNC-TDMA is a collision-free MAC protocol based on TDMA and built using the DESYNC algorithm
Focuses on two shortcomings of traditional TDMA:
  it does not require a global clock
  it automatically adjusts to the number of participating nodes to ensure the available bandwidth is always fully utilized
Desynchronization is a useful primitive for periodic resource sharing in a variety of sensor applications
  example: sensors sampling a common geographic region can desynchronize their sampling schedule such that the requirements of the monitoring task are equally distributed among the sensors

## Slide 50: DESYNC-TDMA
Consider a network of n nodes that communicate with each other
  each node performs a periodic task with a period T
  each node i can be modeled as an oscillator with a frequency ω = 1/T and a phase φi(t) ∈ [0, 1]
    e.g., a phase of 0.75 indicates that the node is 75% through its cycle
    once a node reaches phase 1, it “fires” and resets its phase to 0
  nodes can be imagined as beads moving along a ring with period T where a node fires once it reaches the top
  the only information nodes can observe about the current state of the ring is the firing of events and they can use this to jump forward or backward in phase
  the goal is to have nodes adjust their phase independently such that eventually the network is desynchronized (i.e., nodes are equally spaced around the ring)
  specifically, a node i keeps track of the firings of its immediate neighbors, i.e., nodes i + 1(mod n) and i − 1(mod n)

## Slide 51: DESYNC-TDMA
Assume that Δi represents the distance between oscillators on the ring, i.e., Δi(t)=Φi(t)-Φi-1(t)
Then, node i records its neighbors’ firing times as and ,
Node i can then approximate the phases of its neighbors as
The midpoint between these neighbors can then be determined as:
Once the midpoint has been determined, node i can jump to it

## Slide 52: DESYNC-TDMA
The first ring shows the global view of 5 nodes that are not desynchronized
The second and third rings show B’s local view
When A fires, the node that fired immediately before it (node B), knows the positions of both of its neighbors (i.e., node B overheard the firing of both A and C)
Node B can now compute its ideal position for a desynchronized network and jumps to this position
However, C may have changed its own position in the meantime, unknown to B
If each node can fire closer to the midpoint of its neighbors, this process will eventually bring the system to a state where all nodes are exactly at the midpoint of their neighbors
The last ring shows the global view for the desynchronized state (distances between any two neighboring nodes are identical)

## Slide 53: DESYNC-TDMA
Applied to a wireless sensor network:
  the firing corresponds to a node broadcasting a firing message
    node i keeps track of the times of the firings occurring immediately before and after its own firing
    the senders of these firing messages are then phase neighbors of node i
Applied to TDMA:
  node i’s TDMA slot is defined as beginning at the previously computed midpoint between node i and its previous phase neighbor and as ending at the previously computed midpoint between itself and its next phase neighbor (therefore, a node will never fire outside its own slot)
This algorithm defines a set of non-overlapping slots that cover T and nodes can transmit data without collisions, even during desynchronization
Once desynchronization has completed, the slots have converged to be of equal size

## Slide 54: DESYNC-TDMA
DESYNC ensures the bandwidth is always fully used
  when a node leaves the network, the desynchronization process ensures that slot boundaries are adjusted over time such that their sizes are equalized again
  when a node joins the network, it first sends a series of short interrupt messages before sending its initial firing message
    these interrupt messages notify the owner of the current slot that a new node wants to join
    the slot owner should temporarily pause its transmissions to avoid message collisions

## Slide 55: DESYNC-TDMA
Summary
  DESYNC is an adaptive TDMA-based protocol
  it does not require explicit scheduling or time synchronization
  it provides collision-free communication even during desynchronization
  it further can provide high throughput while guaranteeing predictable message latencies and fairness
  DESYNC adjusts the schedule to accommodate new nodes and to recapture slots given up by leaving nodes
  but: fairness is often not a key concern in wireless sensor networks and ensuring equal slot sizes can lead to inefficient bandwidth usage
    i.e., unused slot portions are therefore wasted
    similarly, if a node has more data to transmit than fits into its slot, the queuing latencies can be high

## Slide 56: Low-Energy Adaptive Clustering Hierarchy
The LEACH protocol combines TDMA-style contention-free communication with a clustering algorithm for wireless sensor networks
  a cluster consists of a single cluster head and any number of cluster members, which only communicate with their cluster head
  clustering is a popular approach for sensor networks
    facilitates data aggregation and in-network processing at the cluster head
    reduces the amount of data that needs to be transmitted to the base station
LEACH operates in rounds consisting of two phases:
  A setup phase phase
  A steady-state phase

## Slide 57: Low-Energy Adaptive Clustering Hierarchy
Setup phase
  cluster heads are determined and communication schedules within each cluster are established
  since the cluster head is responsible for coordinating cluster activity and forwarding data to the base station, its energy requirements will be significantly larger compared to other sensor nodes
  therefore, LEACH rotates the cluster head responsibility among sensor nodes to evenly distribute the energy load
    every sensor i elects itself to be a cluster head with a certain probability Pi(t)
    In a network with N nodes and a desired number of cluster heads of k, the probabilities can be chosen to satisfy:

## Slide 58: Low-Energy Adaptive Clustering Hierarchy
There are various approaches to choose Pi (t), e.g.,:
This approach uses an indicator function Ci (t) to determine whether node i has been a cluster head in the r mod(N/k) previous rounds
Only nodes that have not been cluster heads recently are candidates for the cluster head role, in order to evenly distribute the cluster head responsibility (and energy overhead) among all nodes

## Slide 59: Low-Energy Adaptive Clustering Hierarchy
This approach does not consider the actual amount of energy available to each node
An alternative approach to determining the probability of becoming a cluster head can be used:
  Ei(t) is node i’s actual current energy and Etotal(t) is the sum of the energy levels of all nodes
  a disadvantage of this approach is that every node must know (or estimate) Etotal(t)

## Slide 60: Low-Energy Adaptive Clustering Hierarchy
Once a sensor node has determined that it will serve as cluster head for the next round, it informs other sensor nodes of its new role by broadcasting an advertisement message (ADV) using a non-persistent CSMA protocol
Every sensor node joins a cluster by selecting the cluster head that can be reached with the smallest amount of transmit energy, based on received signal strength of the ADV messages from the cluster heads
Joining is achieved by transmitting a join-request (Join-REQ) message to the chosen cluster head using CSMA
The cluster head establishes a transmission schedule for its cluster and transmits this schedule to each node in its cluster

## Slide 61: Low-Energy Adaptive Clustering Hierarchy
Steady-state phase
  a sensor node communicates only with the cluster head
    it is allowed to transmit data only during its allocated slots (indicated by the schedule received from the cluster head)
  the responsibility of the cluster head is to forward sensor data originating at one of its sensor nodes to the base station
  in order to preserve energy:
    each cluster member uses the minimum required transmit power to reach the cluster head
    each cluster member turns off the wireless radio between its designated slots
  the cluster head remains awake at all times
    to receive sensor data from its cluster members
    to communicate with the base station

## Slide 62: Low-Energy Adaptive Clustering Hierarchy
Sensor nodes use the direct sequence spread spectrum (DSSS) technique to limit the interference among clusters, while intra-cluster communication is contention-free using TDMA-style frames and slots
Communication occurring in one cluster can still interfere with communication in another cluster
Each cluster uses a spreading sequence that is different from the spreading sequences used in neighboring clusters
Another reserved sequence is used for communication between cluster heads and the base station
Communication between cluster heads and base station is based on CSMA
Before a cluster head transmits data, it first senses the channel to see if there is an ongoing transmission using the same spreading code

## Slide 63: Low-Energy Adaptive Clustering Hierarchy
LEACH-C
  variation of LEACH protocol
  relies on the base station to determine the cluster heads
    during setup phase, each sensor node transmits its location and energy levels to the base station
    based on this information, the base station determines the cluster heads and informs the cluster heads of their new role
    other sensor nodes can then join clusters using join messages as described in the original LEACH protocol

## Slide 64: Low-Energy Adaptive Clustering Hierarchy
Summary
  LEACH relies on a variety of techniques to reduce energy consumption
    minimum transmit energy
    avoiding idle listening of cluster members
  LEACH attempts to obtain contention-free communication
    schedule-based communication
    DSSS
  intra-cluster communication is contention-free and interferences among clusters are avoided
  communication between the cluster heads and the base station is still based on CSMA
  assumes that all nodes are able to reach the base station (affects the scalability of this protocol; can be addressed using multi-hop routing or by implementing a hierarchical clustering approach)

## Slide 65: Lightweight Medium Access Control
The LMAC protocol is based on TDMA
  each slot is owned by exactly one node
  nodes execute a distributed algorithm to allocate slots instead of relying on a central manager to assign slots to nodes
  each node uses its slots to transmit a message consisting of two parts:
    control message
      identity of the time slot controller
      distance (in hops) of the node to the gateway (base station)
      address of the intended receiver
      length of the data unit
    data unit
  upon receiving a control message, a node determines if it is the intended receiver and decides whether to stay awake or to turn off the radio until the next slot

## Slide 66: Lightweight Medium Access Control
Description | Size (bytes)
Identification of time slot controller | 2
Current slot number | 1
Occupied slots | 4
Distance to gateway in hops | 1
Collision in slot | 1
Destination address | 2
Data size (bytes) | 1
Total | 12

## Slide 67: Lightweight Medium Access Control
The Occupied Slots field of the control message is a bit-mask of slots
  where an unoccupied slot is represented by 0
  an occupied slot is represented by 1
A node is able to determine unoccupied slots by combining control messages from all neighbors
The process of claiming slots starts at the gateway device, which determines its own slots
After one frame, all direct neighbors of the gateway know the gateway’s slots and choose their own slots
This process continues throughout the network and during each frame, a new set of nodes with a higher hop distance from the gateway determine their slots
Each node must select slots that are not in use within a two-hop neighborhood
Slots are selected randomly, so it is possible for multiple nodes to select the same slot
  will result in a collision of control messages during the slot
  can be observed by the competing nodes, therefore, they will restart the slot selection process

## Slide 68: Mobile LMAC
Slot allocations in LMAC are computed only once, therefore, this protocol is not suitable for mobile sensor network, where nodes frequently join and leave other nodes’ radio ranges
Mobile LMAC (MLMAC) uses a distributed slot allocation mechanism, but it is able to adapt to changes in the network topology
  When a node X leaves the radio range of node Y, both nodes will realize that they no longer receive control messages from each other and they will remove each other from their neighbor lists
  Assume that node X moves into the radio range of node Z and that another node in Z’s range, node W, uses the same slot as X
  Control messages from X and W will collide at Z and node Z will no longer receive any correct control messages during this slot and will therefore mark this slot as unused
  Nodes X and W will receive Z’s control message, indicating that their slot is unused and meaning that there must have been a collision.
  As a consequence, they give up their current slot and restart the slot selection mechanism

## Slide 69: LMAC and MLMAC
Both LMAC and MLMAC have the same advantages as TDMA
  collision-free communication
  energy efficiency
Additionally, they are able to establish transmission schedules in a distributed fashion
However, in both protocols
  slot size is fixed
  slot allocations are also fixed
    except when a node has to restart the slot selection mechanism
  leading to bandwidth inefficiency

## Slide 70: Contention-Based MAC Protocols
These protocols do not rely on transmission schedules, instead they require other mechanisms to resolve contention when it occurs
The main advantage of contention-based techniques is their simplicity compared to most schedule-based techniques
  schedule-based MAC protocols must save and maintain schedules or tables indicating the transmission order
  most contention-based protocols do not require to save, maintain, or share state information
  this also allows contention-based protocols to adapt quickly to changes in network topologies or traffic characteristics
However, they typically result in higher collision rates and overheads due to idle listening and overhearing (overheads usually refer to additional bits in a packet or additional packets such as control packets)
They may also suffer from fairness issues (i.e., some nodes may be able to obtain more frequent channel accesses than others)

## Slide 71: Power Aware Multi-Access with Signaling
The PAMAS protocol attempts to avoid unnecessary energy expenditure caused by overhearing
PAMAS uses two separate channels to prevent collisions among data transmissions: one for data frames and one for control frames (ready-to-send or RTS and clear-to-send or CTS)
The separate signaling channel allows nodes to determine when and how long to power down their wireless transceivers
  devices transmit busy tones on the control channel to ensure that devices that did not overhear either RTS or CTS will not access the data channel for transmissions

## Slide 72: Power Aware Multi-Access with Signaling
Initiating a data transfer
  a PAMAS device sends an RTS message over the control channel to the receiver
  receiver responds with CTS if it does not detect activity on the data channel and has not overheard other recent RTS or CTS messages
  if the source does not receive a CTS within a specific timeout interval, it will attempt to transmit again after a back-off time (exponential back-off algorithm)
  otherwise, it begins data transmission and the receiver node issues a busy tone over the control channel (whose length is greater than twice the length of a CTS)
  the receiver device also issues a busy tone over the control channel whenever it receives an RTS message or detects noise on the control channel while it receives a frame
    done to corrupt possible CTS message replies to the detected RTS, thereby blocking any data transmission of the receiver’s neighbors

## Slide 73: Power Aware Multi-Access with Signaling
Every node in a PAMAS network independently decides when to power off its transceiver
Specifically, a node decides to turn off its transceiver whenever one of two conditions holds:
  a neighbor begins a transmission and the node has no frames to transmit
  a neighbor transmits a frame to another neighbor, even if the node has frames to transmit
A node can easily detect either condition by
  overhearing its neighbor’s transmissions (condition 1) or
  overhearing its neighbor’s busy tone (condition 2)
A node can identify how long to power down its transceiver by embedding the size or expected transmission duration into messages

## Slide 74: Power Aware Multi-Access with Signaling
However, when a transmission begins while a node is still asleep, it does not know how long this transmission will last and how long it should continue to sleep
Therefore, the node issues a probe frame (containing a certain time interval) over the control channel to all transmitting nodes in its neighborhood
  all transmitters that will complete during this interval respond with their predicted completion time
  if such a response is received by the awakening node without collision, it can return to the sleep mode until the completion time indicated by the transmitting node
  if multiple transmitters respond and their responses collide, the node reissues the probe frame with a shorter time interval
  similarly, if the node did not receive a response, it can reissue the probe with a different time interval
  in effect, the node chooses time intervals to perform a binary search to identify when the last ongoing transmission will end

## Slide 75: Sensor MAC
The goal of the S-MAC protocol is
  to reduce unnecessary energy consumption
  while providing good scalability and collision avoidance mechanism
S-MAC adopts a duty-cycle approach
  nodes periodically transition between a listen state and a sleep state
  each node chooses its own schedule, although it is preferred when nodes synchronize their schedules such that nodes listen or sleep at the same time
  nodes using the same schedule are considered to belong to the same virtual cluster (but no real clustering takes place)
    all nodes are free to communicate with nodes outside their clusters
the S-MAC

## Slide 76: Sensor MAC
All nodes are free to communicate with nodes outside their clusters
Nodes periodically exchange their schedules with their neighbors using SYNC messages (every node knows when any of its neighbors will be awake)
If node A wants to communicate with a neighbor B that uses a different schedule, A simply waits until B is listening and then initiates the data transfer
  contention for the medium is resolved using the RTS/CTS scheme
In order to choose a schedule, a node initially listens to the medium for a certain amount of time
  if this node receives a schedule from a neighbor, it chooses this schedule as its own and this node becomes a follower
  the node broadcasts its new schedule after a random delay td to minimize the possibility for collisions from multiple new followers

## Slide 77: Sensor MAC
Nodes can adopt multiple schedules if a node receives a different schedule after it has broadcast its own schedule
  it then adopts both schedules
If a node does not hear a schedule from another node
  it determines its own schedule
  broadcasts this schedule to any potential neighbors
  and this node becomes a synchronizer (in that other nodes will begin to synchronize themselves with it)

## Slide 78: Sensor MAC
S-MAC divides a node’s listen interval further into
  a part for receiving SYNC packets
  a part for receiving RTS messages
Each part is further divided into small slots to facilitate carrier sensing

## Slide 79: Sensor MAC
A node trying to send a SYNC or RTS message randomly selects a time slot within the SYNC or RTS part of the interval, respectively
  senses the carrier for activity from when the receiver begins listening to the selected slot
  if no activity has been detected, it wins the medium and begins transmission
Contention for the medium is addressed using collision avoidance based on RTS/CTS handshakes (S-MAC adopts a contention-based approach)
  when a node hears an RTS or CTS and concludes that it cannot transmit or receive at the same time, it can go to sleep to avoid wasting energy caused by overhearing

## Slide 80: Sensor MAC
Summary
  S-MAC is a contention-based protocol
  utilizes the sleep mode of wireless radios to trade energy for throughput and latency
  collision avoidance is based on RTS/CTS (which is not used by broadcast packets, thereby increasing the collision probability)
  duty cycle parameters (sleep and listen periods) are decided beforehand and may be inefficient for the actual traffic characteristics in the network

## Slide 81: Timeout MAC
If there is only little traffic, S-MAC can actually waste energy because the listening period of S-MAC is of fixed duration
On the other hand, if traffic is heavy, the fixed duration may not be large enough
Therefore, the T-MAC protocol is a variation of S-MAC that uses an active period that adapts to traffic density
Nodes wake up during the beginning of a slot to listen very briefly for activity and return to the sleep mode when no communication has been observed
When a node transmits, receives, or overhears a message, it remains awake for a brief period of time after completion of the message transfer to see if more traffic can be observed
  this brief timeout interval allows a node to return to the sleep mode as quickly as possible
  the end effect is that a node’s awake times will increase with the heavier traffic and will be very brief if traffic is light

## Slide 82: Timeout MAC
To reduce potential collisions, each node waits for a random period of time within a fixed contention interval before the medium is accessed

## Slide 83: Timeout MAC
Once a node hears a CTS, it knows that another node won the medium
This node then stays awake until the end of the transmission, which can be observed by overhearing the acknowledgment (ACK) sent by node B
This event initiates the beginning of the next contention interval and node C will have an opportunity to transmit its data if it wins the medium
In figure, assume that messages flow from top to bottom
  node A sends only to node B, node B sends to node C
  every time node C wants to send a message to node D, C must contend for the medium
    C may lose to node B (B may transmit an RTS before C does) or
    C may lose to node A (C overhears a CTS transmitted by node B)
  while node C stays awake after overhearing node B’s CTS message, its intended receiver (node D) is not aware of C’s intention to transmit data and therefore returns to the sleep mode after TA has expired

## Slide 84: Timeout MAC
Early sleeping problem
  possible solution: future-request-to-send technique
    a node with pending data can inform its intended receiver by transmitting a future-request-to-send (FRTS) packet immediately after overhearing a CTS message
    node D, upon receiving the FRTS message, knows that node C will attempt to send data to it and will therefore remain active
    however, sending an FRTS message immediately after CTS could interfere with node B’s reception of node A’s data
    therefore, Node A first sends a dummy message called Data-Send (DS) to delay the transmission of the actual data
      DS has the same size as FRTS
      DS can collide with FRTS at node B, which is of no consequence since it does not contain any useful information

## Slide 85: Timeout MAC
Summary
  T-MAC’s adaptive approach allows it to adjust a node’s sleep and awake intervals based on the traffic load
  nodes send messages as bursts of variable length and sleep between such bursts to conserve energy
  both S-MAC and T-MAC concentrate message exchanges to small periods of time, resulting in inefficiencies under high traffic loads
  intended receivers are kept awake using messages that indicate future transmissions, which can significantly increase the idle listening times (and energy consumption) of nodes

## Slide 86: Pattern MAC
The PMAC protocol is another example of a TDMA style protocol, but it adapts its sleep schedules on the basis of its own traffic and the traffic patterns of its neighbors
Compared to S-MAC and T-MAC, PMAC further reduces energy costs of idle listening by allowing devices to turn off their radios for long durations during periods of inactivity
Nodes use patterns to describe their tentative sleep and awake times
  a pattern is a string of bits, each bit representing a time slot
    a node plans to sleep: bit is 0
    a node plans to awake: bit is 1

## Slide 87: Pattern MAC
While patterns are only tentative, schedules represent the actual sequence of sleep and awake times
  format of a pattern is always 0m1 where m = 0, 1, . . . , N − 1 and N time slots are considered to be a period (example: pattern 001 and N=6)
  value of m (number of leading zeros) is an indicator of traffic load around the node
    a small value indicates heavy traffic
    a large value indicates light traffic
  every node’s pattern during the first period is 1 (m=0), i.e., every node assumes a heavy traffic load should be awake at all times

## Slide 88: Pattern MAC
If a node does not have any data to send during the first slot, then it uses this as an indicator that the traffic around it is potentially light (pattern becomes 01)
The node continues to double the sleep interval every time it has no data to send (i.e., doubling the number of zeros; allowing it to sleep longer)
This process is continued until a predefined threshold is reached, then the number of zeros is increased linearly
If there is no data for node i to send, the following sequence of patterns will be generated:
    1, 01, 021, 041, . . . , 0δ1, 0δ01, 0δ021, 0δ031, . . . , 0N−11
Whenever a node has data to send, the pattern is immediately reset to 1, allowing the node to wake up quickly and to handle the traffic load

## Slide 89: Pattern MAC
While a pattern is only a tentative sleep plan, patterns are used to derive actual sleep schedules
A node broadcasts its own pattern at the end of a period during a time interval called the Pattern Exchange Time Frame (PETF)
  the PETF is divided into a sequence of brief slots where the number of slots is set to the maximum number of neighbors a node could have
  these slots are accessed using CSMA, i.e., collisions can occur
If a node does not receive a pattern update from one of its neighbors, the node simply assumes the neighbor’s pattern remains unchanged

## Slide 90: Pattern MAC
Once a node has received the patterns from its neighbors, it determines its own schedule, where each slot can be used for one of three possible operations
  if the neighbor has advertised a 1 for that slot, a node wakes up and transmits a message to a neighbor
  if a node has advertised a 1, but has no data to send, the slot is used to listen
  if none of these two conditions holds, the node sleeps

## Slide 91: Pattern MAC
Summary
  PMAC provides a simple mechanism to build schedules that adapt to the amount of traffic in a neighborhood
  when traffic loads are light, a node is able to spend considerable amounts of time in the sleep mode, thereby preserving energy
  however, collisions during the PETF prevent nodes from receiving pattern updates from all neighbors, while other nodes may have received these updates
    leads to inconsistent schedules among nodes in a neighborhood, which can cause
      further collisions
      wasted transmissions
      unnecessary idle listening

## Slide 92: Routing-Enhanced MAC
The RMAC protocol is another example of a protocol that exploits duty cycles to preserve energy
Compared to S-MAC, it attempts to improve upon end-to-end latency and contention avoidance
They key idea behind RMAC is to align the sleep/wake periods of nodes along the path of sensor data such that a packet can be forwarded to the destination within a single operational cycle
It achieves this by sending a control frame along the route to inform nodes of the upcoming packet, allowing them to learn when to be awake to receive and forward this packet

## Slide 93: Routing-Enhanced MAC
RMAC partitions an operational cycle into three components:
  SYNC period
    nodes synchronize their clocks (to maintain sufficient precision)
  DATA period
    used to announce and initiate the packet transmission process along the packet’s route to the destination
    contention-based
      sender waits for a randomly chosen period of time plus an additional DIFS period (and senses the medium during this time)
      if no activity is detected, the sender transmits a Pioneer Control Frame (PION) containing the addresses of the sender, destination, and next hop, the duration of the transmission, and the number of hops travelled so far (0 at sender)
      the next hop along the route looks up the next hop for this route and forwards the PION to the next hop after waiting for a SIFS period
      this process continues until the PION reaches the destination
  SLEEP period

## Slide 94: Routing-Enhanced MAC

## Slide 95: Routing-Enhanced MAC
Actual data transmission takes place during the SLEEP period
Example in figure:
  node A stays awake to receive the data packet from the sender and after successful transmission A returns an acknowledgment (ACK)
  all data and ACK packets are separated by a SIFS period similar to the PION schedule during the DATA period
  after receiving the ACK from node A, the sender has completed its part and it can return its radio into the sleep mode
  node A relays the received packet to the next hop (node B) and also returns its radio to sleep mode once B has acknowledged the data packet
  this process continues until the data packet has been received and acknowledged by the destination

## Slide 96: Routing-Enhanced MAC
The sender and node A stay awake after the DATA period to immediately begin the transmission of the data packet over the first hop
All other nodes along the route can turn off their radios after the DATA period has completed to further preserve energy
Each node wakes up at the right time to receive the data packet from the upstream node
This time to wake up can be computed by node i as:
  where size(DATA) and size(ACK) are the times required to send a single data and ACK frame

## Slide 97: Routing-Enhanced MAC
Summary
  RMAC addresses the large latencies often experienced in MAC protocols based on duty cycles
  it is able to perform end-to-end packet delivery within a single operational cycle
  it also alleviates contention by separating medium contention and data transfer into two separate periods
  however, collisions can still occur, even on the data packets during the SLEEP period
    a source always commences transmission at the beginning of the SLEEP period, therefore it is possible that data packets coming from two different sources (which succeeded in the PION scheduling process during the DATA period, but cannot see each other) may still collide

## Slide 98: Routing-Enhanced MAC
This problem has been addressed by a similar protocol called Demand-Wakeup (DW-MAC)
  the schedule is a one-to-one mapping between a DATA period and the following SLEEP period:
    TiS is the start time of the scheduling frame (SCH) (the equivalent of the pioneer frame in RMAC) measured from the start of the DATA period
    TiD is the start time of the data transmission in the SLEEP period (measured from the start of the SLEEP period)
    Tsleep and Tdata are the durations of the SLEEP and DATA periods
  data packet transmissions do not necessarily coincide with the start of the SLEEP period, but instead depend on the contention window during the DATA period
    reduces the risk of collisions during the SLEEP period

## Slide 99: Data-Gathering MAC
The DMAC protocol exploits the fact that many wireless sensor networks rely on convergecast as communication pattern, i.e., data from sensor nodes are collected at a central node (the “sink”) in a data-gathering tree
The goal of DMAC is to deliver data along the data gathering tree with low latency and high energy efficiency
The duty cycles of nodes along the multi-hop path to the sink are “staggered”, i.e., nodes wake up sequentially like a chain reaction

## Slide 100: Data-Gathering MAC
Nodes switch between sending, receiving, and sleep states
During the sending state, a node sends a packet to the next hop node on the route and awaits an acknowledgment (ACK)
At the same time, the next hop node is in the receiving state, immediately followed by a sending state to forward the packet to the next hop (unless the node is the destination of the packet)
A node enters the sleep state between these intervals of receiving and sending of packets, where it can power down its radio to preserve energy
The sending and receiving intervals are large enough for exactly one packet
Since there are no queuing delays, a node at depth d in the tree can then deliver a packet to the sink within d intervals
While limiting a node’s activity to brief intervals for sending and receiving reduces the contention, collisions can still occur
  e.g., nodes with the same depth in the tree will have synchronized schedules

## Slide 101: Data-Gathering MAC
If a sender does not receive an ACK, it queues the packet until the next sending interval and after three failed retransmissions, the packet will be dropped
To reduce collisions, nodes do not transmit immediately at the beginning of the sending slot, but instead have a back-off period (BP) plus a random time within a contention window
When a node has multiple packets to send during a sending slot
  it can increase its own duty cycle and
  it requests other nodes along the route to the sink to do the same
This is implemented through a slot-by-slot renewal mechanism using a more data flag in the MAC header
A receiver checks for this flag and if set
  it returns an acknowledgment that has also the more data flag set
  it then stays awake to receive and forward one additional packet

## Slide 102: Data-Gathering MAC
Summary
  DMAC’s staggering technique achieves very low latency
  nodes only stay awake for brief receive and send intervals
  since many nodes in the data-gathering tree share the same schedule, collisions will occur and DMAC only employs limited collision avoidance methods
  DMAC works best for networks in which the transmission paths and rates are well known and do not change over time

## Slide 103: Preamble Sampling and WiseMAC
WiseMAC is a MAC protocol that is concerned with the energy consumption of downlink communication (from base station to sensor nodes) in infrastructure-based sensor networks
To avoid energy consumption due to idle listening, WiseMAC relies on the preamble sampling technique
Preamble sampling
  the base station transmits a preamble preceding the actual data transmission to alert the receiving node

## Slide 104: Preamble Sampling and WiseMAC
Preamble sampling (contd.)
  all sensor nodes sample the medium with a fixed period Tw but with independent and constant relative sampling schedule offsets
  if the medium is busy, a sensor node continues to listen until the medium becomes idle or a data frame is received
  the preamble’s size is equal to the sampling period
    ensures that the receiver will be awake to receive the data portion of the packet
  this approach allows the energy-constrained sensor nodes to turn off the radio when the channel is idle (without the risk of missing a packet)
  disadvantages
    the size of the preamble affects the achievable throughput
    a device must stay awake when a preamble is detected even if it is not the intended receiver

## Slide 105: Preamble Sampling and WiseMAC
WiseMAC improves upon this by adding a technique by letting a base station learn the sampling schedules of the destination, thereby allowing the base station to start the transmission of the preamble immediately before the receiver wakes up
  allows the base station to reduce the size of the preamble
  awake time of the receiver is also shortened since the data portion of the packet will start shortly after the receiver’s radio has turned on
A node’s schedule offset is embedded into the acknowledgment (ACK) message allowing the base station to learn the sampling schedules
The duration of the preamble Tp is then determined as the minimum of the destination’s sampling period Tw and a multiple of the clock drift between the clock clock at the base station and on the receiver (grows over time)
Therefore, the preamble length depends on the traffic load:
  preamble is shorter when traffic is high (brief intervals between two consecutive communications)
  preamble is larger under low load

## Slide 106: Preamble Sampling and WiseMAC
Summary
  WiseMAC implements energy-efficient wake/sleep schedules for sensor nodes while ensuring that all data transmissions from a base station to the sensors will be received (i.e., the receiver will be awake)
  however, the approach is inefficient for broadcast messages since the preamble is likely to be very large (i.e., it must span over the sampling points of all receiver devices)
  WiseMAC is also affected by the hidden terminal problem (i.e., a sender’s preamble can interfere with ongoing transmissions when the sender is not aware of this other transmission)

## Slide 107: Receiver-Initiated MAC
The RI-MAC protocol is another contention-based solution
  a transmission is always initiated by the receiver of the data
  each node wakes up periodically to check whether there is an incoming data packet
  a node checks if the medium is idle immediately after turning on its radio
    if so, it broadcasts a beacon message announcing that it is awake and ready to receive data

## Slide 108: Receiver-Initiated MAC
A node with pending data to transmit stays awake and listens for a beacon from its intended receiver
Once this beacon has been received the sender immediately transmits the data
  data will be acknowledged by the receiver with another beacon
The beacon serves two purposes:
  it invites new data transmissions
  it acknowledges previous transmissions
If there is no incoming data packet for a certain amount of time after the beacon broadcast, the node goes back to sleep after waiting a certain time

## Slide 109: Receiver-Initiated MAC

## Slide 110: Receiver-Initiated MAC
If there are multiple contending senders, a receiver uses its beacon frames to coordinate transmissions
A field in the beacon, called the back-off window size (BW) specifies the window over which to select a back-off value
If the beacon does not contain a BW (the first beacon sent out after waking up does not contain a BW), senders immediately commence transmission
Otherwise, each sender randomly selects a back-off value within BW and the receiver increases the BW value in the next beacon when it detects a collision
  the receiver notices the collision and sends another beacon (containing a BW)
  if multiple collisions occur and the receiver was not able to receive a packet for several beacon intervals, the node simply goes to sleep without further attempts

## Slide 111: Receiver-Initiated MAC
The receiver is in control of when to receive data and it is responsible for detecting collisions and recovering lost data
Since transmissions are triggered by beacons, the receiver will have very little overhead due to overhearing
Senders must wait for the receiver’s beacon before they can transmit (potentially leading to large overhearing costs)
When packets collide
  the senders will retry until the receiver gives up
  potentially leading to more collisions in the network and to increased data delivery latencies

## Slide 112: Hybrid MAC Protocols
Display characteristics of both categories
  attempt to reduce the number of collisions by relying on features present in contention-free medium access protocols
  take advantage of the flexibility and low complexity of contention-based protocols

## Slide 113: Zebra MAC
The Z-MAC protocol uses frames and slots to provide contention-free access to the wireless medium
  similar to TDMA-based protocols
However, Z-MAC also allows nodes to utilize slots they do not own using CSMA with prioritized back-off times
As a consequence:
  in low-traffic scenarios, Z-MAC emulates a CSMA-based approach
  when traffic loads are high, Z-MAC emulates a TDMA-based approach

## Slide 114: Zebra MAC
When a node starts up, it enters a setup phase to allow it
  to discover its neighbors
  to obtain its slot in the TDMA frame
Every node periodically broadcasts a message containing a list of its neighbors
  through this process, a node learns about its 1-hop and 2-hop neighbors
  this information is used as input to a distributed slot assignment protocol (provides each node with time slots)
  ensures a schedule where no two nodes within an 2-hop neighborhood will be assigned the same slot

## Slide 115: Zebra MAC
Z-MAC allows nodes to select the periodicity of their assigned slots where different nodes can have different periods (time frames or TF)
The advantage of this approach is that it is not necessary to propagate a maximum slot number (MSN) to the entire network
The protocol can adapt slot allocations locally
  assume that node i is assigned slot si
  and Fi represents the MSN within the node’s 2-hop neighborhood
  then: i’s TF is set to be 2a
    a is a positive integer that satisfies 2a−1 ≤ Fi < 2a − 1
  node i then uses the sith slot in every 2a time frame

## Slide 116: Zebra MAC
Example with eight nodes
  number indicates the assigned slot for each node
  number in parenthesis is Fi
  bottom part of the figure shows the corresponding schedule for all nodes
    light-shaded slots are the ones used for transmissions
    dark-shaded slots are the empty slots that are not used by any 1-hop or 2-hop neighbors
  if a global time frame is used, the chosen time frame size will be 6
    nodes A and B will be allowed to use their slots only once every 6 slots even though their frame sizes are 2 each

## Slide 117: Zebra MAC

## Slide 118: Zebra MAC
In Z-MAC, these nodes can use frame size 4
  increases the concurrency in the channel usage
  reduces message delays
The resulting schedule shows that some slots are not assigned to any node
  specifically slots 6 and 7
In a global time frame, a frame size could have been chosen that reduces the number of empty slots
However, Z-MAC allows nodes to compete for these “extra” slots using CSMA

## Slide 119: Zebra MAC
After the schedule has been determined, every node forwards its frame size and slot number to its 1-hop and 2-hop neighbors
Even though slots are owned by nodes, Z-MAC uses CSMA to determine who may transmit
However, slot owners are given preference
  by using a random back-off value chosen from the range [0, To]
  whereas other nodes choose their back-off values from the range [To, Tno]

## Slide 120: Zebra MAC
Z-MAC also uses explicit contention notification (ECN) to which it has a message
  where each node decides to whether to send an ECN message to a neighbor based on its local estimate of the contention level (e.g., determined using the packet loss rate or channel noise level)
  this neighbor then broadcasts the ECN to its own neighbors, which then enter a high contention level (HCL) mode
  a node in the HCL mode only transmits data in its own slots or slots belonging to its 1-hop neighbors
    thereby reducing the contention between 2-hop neighbors
  it returns to a low contention level (LCL) mode if it has not received any ECN messages for a certain amount of time

## Slide 121: Zebra MAC
Summary
  Z-MAC adopts characteristics found in both TDMA and CSMA protocols
  allowing it to quickly adapt to changing traffic conditions
  under light traffic loads Z-MAC behaves more like CSMA
  under heavy traffic loads contention for slots is reduced
  Z-MAC requires an explicit setup phase (consumes both time and energy)
  while ECN messages be used to reduce the contention locally
    these messages add more traffic to an already busy network and take time to propagate
    thereby causing delays in the adaptation to a more TDMA-like behavior

## Slide 122: Mobility Adaptive Hybrid MAC
In many sensor networks, some or all nodes can be mobile
  can bear significant challenges for the design of a MAC protocol
The MH-MAC protocol proposes a hybrid solution
  uses a schedule-based approach for static nodes
  uses a contention-based approach for mobile nodes
While it is straightforward to determine a TDMA-style schedule for static nodes, this is not the case for mobile nodes
  MH-MAC allows mobile nodes entering a neighborhood to use a contention-based approach to avoid the delays often needed to be inserted into the schedule

## Slide 123: Mobility Adaptive Hybrid MAC
The slots of a frame belong to one of the two categories:
  static slots
  mobile slots
Each node uses a mobility estimation algorithm to determine its mobility and which type of slots the node should use
  mobility estimation is based on periodic hello messages and received signal strength
    hello messages are always transmitted with the same transmit power
    receiving nodes compare consecutive message signal strengths to estimate the relative position displacement between themselves and each of their neighbors
  a mobility beacon interval is provided at the beginning of a frame to distribute mobility information to neighbors

## Slide 124: Mobility Adaptive Hybrid MAC
Static slots
  use an approach similar to the LMAC approach and have two portions:
    a control section
      indicate the slot assignment information in a neighborhood
      all static nodes must listen to this part of the static slot
    a data section
      only the transmitter and receiver stay awake
      all other nodes can turn their radios off
Mobile slots
  nodes contend for the medium in a two-phase contention period
    a wakeup tone is sent during the first phase
    the data is sent during the second phase
  priority ordering among mobile nodes to reduce the effective contention

## Slide 125: Mobility Adaptive Hybrid MAC
MH-MAC provides a mechanism to dynamically adjust the ratio between static and mobile slots
  based on the observed mobility
  necessary since the ratio of static versus mobile nodes can vary
  each node estimates its own mobility and sends this information in the previously mentioned beacon time slot at the beginning of a frame
  using this mobility information, each node calculates a mobility parameter for the network, which determines the ratio of static and mobile slots

## Slide 126: Mobility Adaptive Hybrid MAC
Summary
  MH-MAC combines characteristics of the LMAC protocol for static nodes and features of contention-based protocols for mobile nodes
  mobile nodes can quickly join a network without long setup or adaptation delays
  compared to LMAC
    MHMAC allows nodes to own more than one slot in a frame
    this increases bandwidth utilization and decreases latencies

## Slide 127: Summary
The choice of a medium access protocol has a substantial impact on the performance and energy-efficiency of a WSN
MAC protocols should also be designed to accommodate changes in network topology and traffic characteristics
Latency, throughput, and fairness among competing nodes determined or affected by the characteristics of the MAC layer
Protocols based on transmission schedules
  collision-free
  resource-inefficient
  may require well synchronized nodes throughout the network
  difficult to adapt to changing topologies

## Slide 128: Summary
  Protocols that let nodes compete for access to the medium
  more flexible (easily accommodate changing network topologies)
  require less overhead
  not collision-free
  must possess features that allow them to recover from collisions
  network utilization may suffer when collisions occur frequently