## Slide 1: Chapter 3: Node Architecture
Notes: <number>

## Slide 2: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 3: Node Architecture
Wireless sensor nodes are the essential building blocks in a wireless sensor network
  sensing, processing, and communication
  stores and executes the communication protocols as well as data processing algorithms
The node consists of sensing, processing, communication, and power subsystems
  trade-off between flexibility and efficiency – both in terms of energy and performance
Notes: <number>

## Slide 4: Node Architecture
Figure 3.1 Architecture of a wireless sensor node
Notes: <number>

## Slide 5: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 6: The Sensing Subsystem
The sensing subsystem integrates
Sensor | Application Area | Sensed Event | Explanation
Accelerometer | AVM | 2D and 3D acceleration of movements of people and objects | Volcano activities
 | SHM |  | Stiffness of a structure
 | Health care |  | Stiffness of bones, limbs, joints; Motor fluctuation in Parkinson’s disease
 | Transportation |  | Irregularities in rail, axle box or wheels of a train system
 | SCM |  | Defect of fragile objects during transportation
Acoustic emission sensor | SHM | Elastic waves generated by the energy released during crack propagation | Measures micro-structural changes or displacements
Acoustic sensor | Transportation & Pipelines | Acoustic pressure vibration | Vehicle detection; Measure structural irregularities; Gas contamination
Capacitance sensor | PA | Solute concentration | Measure the water content of a soil
Notes: <number>

## Slide 7: The Sensing Subsystem
Sensor | Application Area | Sensed Event | Explanation
ECG | Health care | Heart rate | 
EEG |  | Brain electrical activity | 
EMG |  | Muscle activity | 
Electrical sensors | PA | Electrical capacitance or inductance affected by the composition of tested soil | Measure of nutrient contents and distribution
Gyroscope | Health care | Angular velocity | Detection of gait phases
Humidity sensor | PA & HM | Relative and absolute humidity | 
Infrasonic sensor | AVM | Concussive acoustic waves – earth quake or volcanic eruption | 
Magnetic sensor | Transportation | Presence, intensity, direction, rotation and variation of a magnetic field | Presence, speed and density of a vehicle on a street; congestion
Oximeter | Health care | Blood oxygenation of patient's hemoglobin | Cardiovascular exertion and trending of exertion relative to activity
pH sensor | Pipeline (water) | Concentration of hydrogen ions | Indicates the acid and alkaline content of a water measure of cleanliness
Notes: <number>

## Slide 8: The Sensing Subsystem
Sensor | Application Area | Sensed Event | Explanation
Photo acoustic spectroscopy | Pipeline | Gas sensing | Detects gas leak in a pipeline
Piezoelectric cylinder | Pipeline | Gas velocity | A leak produces a high frequency noise that produces a high frequency noise that produces vibration
Soil moisture sensor | PA | Soil moisture | Fertilizer and water management
Temperature sensor | PA & HM | Pressure exerted on a fluid | 
Passive infrared sensor | Health care & HM | Infrared radiation from objects | Motion detection
Seismic sensor | AVM | Measure primary and secondary seismic waves (Body wave, ambient vibration) | Detection of earth quake
Oxygen sensor | Health care | Amount and proportion of oxygen in the blood | 
Blood flow sensor | Health care | The Doppler shift of a reflected ultrasonic wave in the blood | 
Notes: <number>

## Slide 9: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 10: Analog-to-Digital Converter
ADC converts the output of a sensor - which is a continuous, analog signal - into a digital signal. It requires two steps:
  the analog signal has to be quantized
    allowable discrete values is influenced :
  (a) by the frequency and magnitude of the signal
  (b) by the available processing and storage resources
  2. the sampling frequency
    Nyquist rate does not suffice because of noise and transmission error
    resolution of ADC - an expression of the number of bits that can be used to encode the digital output
where Q is the resolution in volts per step (volts per output code); Epp is the peak-to-peak analog voltage; M is the ADC’s resolution in bits
Notes: <number>

## Slide 11: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 12: The Processor Subsystem
The processor subsystem
  interconnects all the other subsystems and some additional peripheries
  its main purpose is to execute instructions pertaining to sensing, communication, and self-organization
It consists of
  processor chip
  nonvolatile memory - stores program instructions
  active memory - temporarily stores the sensed data
  internal clock
Notes: <number>

## Slide 13: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 14: Architectural Overview
The processor subsystem can be designed by employing one of the three basic computer architectures
  Von Neumann architecture
  Harvard architecture
  Super-Harvard (SHARC) architecture
Notes: <number>

## Slide 15: Von Neumann Architecture
Von Neumann architecture
  provides a single memory space - storing program instructions and data
  provides a single bus - to transfer data between the processor and the memory
  Slow processing speed - each data transfer requires a separate clock

## Slide 16: Von Neumann Architecture
Notes: <number>

## Slide 17: Harvard Architecture
Harvard architecture
  provides separate memory spaces - storing program instructions and data
  each memory space is interfaced with the processor with a separate data bus
  program instructions and data can be accessed at the same time
  a special single instruction, multiple data (SIMD) operation, a special arithmetic operation and a bit reverse
  supports multi-tasking operating systems; but does not provide virtual memory protection
Notes: <number>

## Slide 18: Harvard Architecture

## Slide 19: Super-Harvard Architecture
Super-Harvard architecture (best known: SHARC)
  an extension of the Harvard architecture
  adds two components to the Harvard architecture:
    internal instruction cache - temporarily store frequently used instructions - enhances performance
    an underutilized program memory can be used as a temporary relocation place for data
    Direct Memory Access (DMA)
      costly CPU cycles can be invested in a different task
      program memory bus and data memory bus accessible from outside the chip
Notes: <number>

## Slide 20: Super-Harvard Architecture
Processor
Data Memory
Address Bs
Data Bus
Program Memory
I/O Controller
Instruction Cache
Notes: <number>

## Slide 21: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 22: Microcontroller
Structure of microcontroller
  integrates the following components:
    CPU core
    volatile memory (RAM) for data storage
    ROM, EPROM, EEPROM, or Flash memory
    parallel I/O interfaces
    discrete input and output bits
    clock generator
    one or more internal analog-to-digital converters
    serial communications interfaces
Notes: <number>

## Slide 23: Microcontroller
Advantages:
  suitable for building computationally less intensive, standalone applications, because of its compact construction, small size, low-power consumption, and low cost
  high speed of the programming and eases debugging, because of the use of higher-level programming languages
Disadvantages:
  not as powerful and as efficient as some custom-made processors (such as DSPs and FPGAs)
  some applications (simple sensing tasks but large scale deployments) may prefer to use architecturally simple but energy- and cost-efficient processors
Notes: <number>

## Slide 24: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 25: Digital Signal Processor
The main function:
  process discrete signals with digital filters
  filters minimize the effect of noise on a signal or enhance or modify the spectral characteristics of a signal
  while analog signal processing requires complex hardware components, digital signal processors (DSP) requires simple adders, multipliers, and delay circuits
  DSPs are highly efficient
  most DSPs are designed with the Harvard Architecture
Notes: <number>

## Slide 26: Digital Signal Processor
Advantages:
  powerful and complex digital filters can be realized with commonplace DSPs
  useful for applications that require the deployment of nodes in harsh physical settings (where the signal transmission suffers corruption due to noise and interference and, hence, requires aggressive signal processing)
Disadvantage:
  some tasks require protocols (and not numerical operations) that require periodical upgrades or modifications (i.e., the networks should support flexibility in network reprogramming)
Notes: <number>

## Slide 27: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 28: Application-specific Integrated Circuit
ASIC is an IC that can be customized for a specific application
Two types of design approaches: full-customized and half-customized
  full-customized IC:
    some logic cells, circuits, or layout are custom made in order to optimize cell performance
    includes features which are not defined by the standard cell library
    expensive and long design time
  half-customized ASICs are built with logic cells that are available in the standard library
  in both cases, the final logic structure is configured by the end user - an ASIC is a cost efficient solution, flexible, and reusable
Notes: <number>

## Slide 29: Application-specific Integrated Circuit
Advantages:
  relatively simple design; can be optimized to meet a specific customer demand
  multiple microprocessor cores and embedded software can be designed in a single cell
Disadvantage:
  high development costs and lack of re-configurability
Application:
  ASICs are not meant to replace microcontrollers or DSPs but to complement them
  handle rudimentary and low-level tasks
    to decouple these tasks from the main processing subsystem
Notes: <number>

## Slide 30: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 31: Field Programmable Gate Array (FPGA)
The distinction between ASICs and FPGAs is not always clear
  FPGAs are more complex in design and more flexible to program
  FPGAs are programmed electrically, by modifying a packaged part
  programming is done with the support of circuit diagrams and hardware description languages, such as VHDL and Verilog
Notes: <number>

## Slide 32: Field Programmable Gate Array (FPGA)
Advantages:
  higher bandwidth compared to DSPs
  flexible in their application
  support parallel processing
  work with floating point representation
  greater flexibility of control
Disadvantages:
  complex
  the design and realization process is costly
Notes: <number>

## Slide 33: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 34: Comparison
Working with a micro-controller is preferred if the design goal is to achieve flexibility
Working with the other mentioned options is preferred if power consumption and computational efficiency is desired
DSPs are expensive, large in size and less flexible; they are best for signal processing, with specific algorithms
FPGAs are faster than both microcontrollers and digital signal processors and support parallel computing; but their production cost and the programming difficulty make them less suitable
Notes: <number>

## Slide 35: Comparison
ASICs have higher bandwidths; they are the smallest in size, perform much better, and consume less power than any of the other processing types; but have a high cost of production owing to the complex design process

## Slide 36: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 37: Communication Interfaces
Fast and energy efficient data transfer between the subsystems of a wireless sensor node is vital
  however, the practical size of the node puts restriction on system buses
  communication via a parallel bus is faster than a serial transmission
  a parallel bus needs more space
Therefore, considering the size of the node, parallel buses are never supported
Notes: <number>

## Slide 38: Communication Interfaces
The choice is often between serial interfaces :
    Serial Peripheral Interface (SPI)
    General Purpose Input/Output (GPIO)
    Secure Data Input/Output (SDIO)
    Inter-Integrated Circuit (I2C)
Among these, the most commonly used buses are SPI and I2C

## Slide 39: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 40: Serial Peripheral Interface
SPI (Motorola, in the mid-80s)
  high-speed, full-duplex synchronous serial bus
  does not have an official standard, but use of the SPI interface should conform to the implementation specification of others - correct communication
The SPI bus defines four pins:
  MOSI (MasterOut/SlaveIn)
    used to transmit data from the master to the slave when a device is configured as a master
  MISO (MasterIn/SlaveOut)
  SCLK (Serial Clock)
    used by the master to send the clock signal that is needed to synchronize transmission
    used by the slave to read this signal synchronize transmission
  CS (Chip Select) - communicate via the CS port
Notes: <number>

## Slide 41: Serial Peripheral Interface
Both master and slave devices hold a shift register
Every device in every transmission must read and send data
SPI supports a synchronous communication protocol
  the master and the slave must agree on the timing
  master and slave should agree on two additional parameters
    clock polarity (CPOL) - defines whether a clock is used as high- or low-active
    clock phase (CPHA) - determines the times when the data in the registers is allowed to change and when the written data can be read

## Slide 42: Serial Peripheral Interface
Notes: <number>

## Slide 43: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 44: Inter-Integrated Circuit
Every device type that uses I2C must have a unique address that will be used to communicate with a device
In earlier versions, a 7 bit address was used, allowing 112 devices to be uniquely addressed - due to an increasing number of devices, it is insufficient
Currently I2C uses 10 bit addressing
I2C is a multi-master half-duplex synchronous serial bus
  only two bidirectional lines: (unlike SPI, which uses four)
    Serial Clock (SCL)
    Serial Data (SDA)
Notes: <number>

## Slide 45: Inter-Integrated Circuit
Since each master generates its own clock signal, communicating devices must synchronize their clock speeds
  a slower slave device could wrongly detect its address on the SDA line while a faster master device is sending data to a third device
I2C requires arbitration between master devices wanting to send or receive data at the same time
  no fair arbitration algorithm
  rather the master that holds the SDA line low for the longest time wins the medium

## Slide 46: Inter-Integrated Circuit
I2C enables a device to read data at a byte level for a fast communication
  the device can hold the SCL low until it completes reading or sending the next byte - called handshaking
The aim of I2C is to minimize costs for connecting devices
  accommodating lower transmission speeds
I2C defines two speed modes:
  a fast-mode - a bit rate of up to 400Kbps
  high-speed mode - a transmission rate of up to 3.4 Mbps
  they are downwards compatible to ensure communication with older components

## Slide 47: Comparison
SPI | I2C
4 lines enable full-duplex transmission | 2 lines reduce space and simplify circuit layout; Lowers costs
No addressing is required due to CS | Addressing enables multi-master mode; Arbitration is required
Allowing only one master avoids conflicts | Multi-master mode is prone to conflicts
Hardware requirement support increases with an increasing number of connected devices -- costly | Hardware requirement is independent of the number of devices using the bus
The master's clock is configured according to the slave's speed but speed adaptation slows down the master. | Slower devices may stretch the clock -- latency but keeping other devices waiting
Speed depends on the maximum speed of the slowest device | Speed is limited to 3.4 MHz
Heterogeneous registers size allows flexibility in the devices that are supported. | Homogeneous register size reduces overhead
Combined registers imply every transmission should be read AND write | Devices that do not read or provide data are not forced to provide potentially useless bytes
The absence of an official standard leads to application specific implementations | Official standard eases integration of devices since developers can rely on a certain implementation
Notes: <number>

## Slide 48: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 49: Communication Interfaces - Summary
Buses are essential highways to transfer data
  due to the concern for size, only serial buses can be used
  serial buses demand high clock speeds to gain the same throughput as parallel buses
  serial buses can also be bottlenecks (e.g., Von Neumann architecture) or may not scale well with processor speed (e.g., I2C)
Delays due to contention for bus access become critical, for example, if some of the devices act unfairly and keep the bus occupied
Notes: <number>

## Slide 50: Outline
The Sensing Subsystem
  Analog-to-Digital Converter
The Processor Subsystem
  Architectural Overview
  Microcontroller
  Digital Signal Processor
  Application-specific Integrated Circuit
  Field Programmable Gate Array
  Comparison
Communication Interfaces
  Serial Peripheral Interface
  Inter-Integrated Circuit
  Summary
Prototypes
  The IMote Node Architecture
  The XYZ Node Architecture
  The Hogthrob Node Architecture
Notes: <number>

## Slide 51: The IMote Node Architecture
The IMote sensor node architecture is a multi-purpose architecture, consisting of :
  a power management subsystem
  a processor subsystem
  a sensing subsystem
  a communication subsystem
  an interfacing subsystem
Notes: <number>

## Slide 52: The IMote Node Architecture
Notes: <number>

## Slide 53: The IMote Node Architecture
A multiple-sensor board contains :
  a 12-bit, four channels ADC
  a high-resolution temperature/humidity sensor
  a low-resolution digital temperature sensor
  a light sensor
  the I2C bus is used to connect low data rate sources
  the SPI bus is used to interface high data rate sources
Notes: <number>

## Slide 54: The IMote Node Architecture
Notes: <number>

## Slide 55: The IMote Node Architecture
The processing subsystem provides
  main processor (microprocessor)
    operates in low voltage (0.85V) and low frequency (13MHz) mode
    Dynamic Voltage Scaling (104MHz - 416MHz)
    sleep and deep sleep modes
    thus enabling low power operation
  coprocessor (a DSP)
    accelerates multimedia operations - computation intensive

## Slide 56: The XYZ Node Architecture
Consists of the four subsystems:
  power subsystem
  communication subsystem
  mobility subsystem
  sensor subsystem

## Slide 57: The XYZ Node Architecture
Notes: <number>

## Slide 58: The XYZ Node Architecture
The processor subsystem is based on the ARM7TDMI core microcontroller
  fmax = 58MHz
  two different modes (32bits and 16bits)
  provides an on-chip memory of 4KB boot ROM and a 32KB RAM - can be extended by up to 512KB of flash memory
Peripheral components:
  DMA controller
  fopur 10-bit ADC inputs
  serial ports (RS232, SPI, I2C, SIO)
  42 multiplexed general purpose I/O pins
Notes: <number>

## Slide 59: The XYZ Node Architecture
The communication subsystem is connected to the processing subsystem through a SPI interface
  CC2420 RF transceiver
  when an RF message has been successfully received, the SPI interface enables the radio to wake up a sleeping processor
  the processor subsystem controls the communication subsystem by either turning it off or putting it in sleep mode

## Slide 60: The Hogthrob Node Architecture
Designed for a specific application, namely, to monitor pig production
Motivation:
  monitors movements of a sow to predict onset of estrus
    so that appropriate care can be given for pregnant sows
  detecting cough or limping to monitor illness
Notes: <number>

## Slide 61: The Hogthrob Node Architecture
Notes: <number>

## Slide 62: The Hogthrob Node Architecture
The processing subsystems consists of :
  microcontroller
    performs less complex, less energy intensive tasks
    initializes the FPGA and functions as an external timer and an ADC converter to it
  Field Programmable Gate Array
    executes the sow monitoring application
    coordinates the functions of the sensor node
Notes: <number>

## Slide 63: The Hogthrob Node Architecture
There are a number of interfaces supported by the processing subsystem, including
  the I2C interface for the sensing subsystem
  the SPI interface for the communication subsystem
  the JTAG interface for in-system programmability and debugging
  the serial (RS232) interface for interaction with a PC