## Slide 1: Προσομοίωση Δικτύων
2n Άσκηση
Δημιουργία, διαμόρφωση μελέτη επικοινωνιακών ζεύξεων

## Slide 2: Δημιουργία ζεύξης
Create a simulator object
    set ns [new Simulator]
Open a file for writing that is going to be used for the nam trace data.
    set nf [open out.nam w]
    $ns namtrace-all $nf
Open a file for writing that is going to be used for the event trace data.
    set tf [open out.tr w]
    $ns trace-all $tf

## Slide 3: Δημιουργία ζεύξης
Add a 'finish' procedure that closes the trace file and starts nam.
  proc finish {} {
    global ns nf tf
    $ns flush-trace
    close $nf
    close $tf
    exec nam out.nam &
    exit 0
  }
Execute the 'finish' procedure after 5.0 seconds of simulation time.
    $ns at 5.0 "finish"
Starts the simulation.
    $ns run

## Slide 4: Δημιουργία ζεύξης
Run the simulation
  If everything goes well, you should get
    No error messages
    And something
    like the following
So, we have the simulation shell but nothing in it.
Let's create a bidirectional link

## Slide 5: Δημιουργία ζεύξης
Create two nodes
  set n0 [$ns node]
  set n1 [$ns node]
Create a bidirectional link between these nodes
  $ns duplex-link $n0 $n1 1Mb 10ms DropTail
Run again the simulation
  It should now look like this 
  Now we have a network that does nothing

## Slide 6: Δημιουργία ζεύξης
Let put some traffic over the link
  A CBR traffic source from n0
  #Create a UDP agent and attach it to node n0
  set udp0 [new Agent/UDP]
  $ns attach-agent $n0 $udp0
  # Create a CBR traffic source and attach it to udp0
  set cbr0 [new Application/Traffic/CBR]
  $cbr0 set packetSize_ 500
  $cbr0 set interval_ 0.009
  $cbr0 attach-agent $udp0

## Slide 7: Δημιουργία ζεύξης
Let put some traffic over the link
  A traffic sink to n1
  set null0 [new Agent/Null]
  $ns attach-agent $n1 $null0
  Connection at transport layer
  $ns connect $udp0 $null0
  Control the beginning and stop of the data flow
  $ns at 0.5 "$cbr0 start"
  $ns at 4.5 "$cbr0 stop“
Re-run it and see the traffic at nam appllication
Increase traffic rate until you see packet get dropped
  Gradually increase packet creation rate
  Gradually increase packet size
Notes: Με 500 byte πακέτα, αρχίζει και χάνει στα 0.003sec
Με 0.009 αρχίζει και χάνει στα 1500 πακέτα.

## Slide 8: Performance Evaluation
First make sure you have all the right files in the same folder
  delay_2nd_lab.txt
  out.tr
  out.nam
1st way: using the awk script “delay_2nd_lab.tx
  Execute the following command:
    awk –f delay_2nd_lab.txt out.tr
    This command applies “delay_2nd_lab.txt” upon the “out.tr” trace file and should give something like

## Slide 9: Performance Evaluation
2nd way: Reading the out.tr file
  You can open it with an editor and read it based on the following guideline

## Slide 10: Δημιουργία ζεύξης (ΑΝΑΦΟΡΑ)
Calculate the packet delay through the trace file
Study how packet interval affect performance through awk script (ΑΝΑΦΟΡΑ)
  Packet size = 500
  Packet interval 0.009 – 0.005 – 0.003 – 0.002 – 0.001
  Κάντε γραφικές παραστάσεις για όλα τα performance metrics
  Επαληθεύσατε τα delays από το trace file (print screens)
Study how packet size affect performance through awk script (ΑΝΑΦΟΡΑ)
  Packet interval 0.009
  Packet size 500, 700, 1000, 1100, 1500
  Κάντε γραφικές παραστάσεις για όλα τα performance metrics
  Επαληθεύσατε τα delays από το trace file (print screens)

## Slide 11: Δημιουργία ζεύξης (ΑΝΑΦΟΡΑ)
Create an opposite data flow i.e. from n1 to n0
Study performance effect when opposite flow exist
  Calculate drop packets for 500Byte packets and 0.003 packet interval
  Increase link bandwidth gradually by 0.1Mb until zero packet loss is recorded
  Κάντε γραφικές παραστάσεις για όλα τα performance metrics
  Επαληθεύσατε τα delays από το trace file (print screens)